## Slide 1
Microflex 0.5 – Innovative compact automotive connector interface
Microflex 0.5 is a compact and flexible automotive open interface with possibility of Ethernet-integration
Microflex 0.5: Miniaturized, flexible interface based on 0.5 mm standardized pins
Shown connectors available by BOSCH / Sumitomo

## Slide 2: Open Interface - Modular for high flexibility and functionality
Microflex 0.5 – Innovative compact automotive connector interface
Modules with signal pins 0.5x0.4 and
with optional power tabs 1.2x0.6
32 pole
52 pole
72 pole
104 pole
Sealed harness connector with outside locking
Unsealed harness connector with inside locking
ECU with Microflex 0.5 interface (sealed & unsealed)
on same Interface
out-side /
in-side Locking geometry for unsealed & sealed harness connectors
OPEN INTERFACE: drawing free available
http://bosch-open-interfaces.de
4-row Interface modules
Standardization
Miniaturization
High flexibility
Equal parts, cost
Ethernet functionality
Modular design, scalability
Base for:
2-row Interface modules

## Slide 3: Typical specification of Microflex-interface*
Specification: SAE/USCAR-2 REVISION 6 LV214
Temperature Class: ** (T3) **
Sealing Class: Unsealed / sealed (S1-S3) PG23 (sealed)
Current rating (in connector) 0.5 terminals: 2.5 A / 3.5 A @ 90°C Sn/Ag (0.35 mm²)
1.2 terminals: 5-6 A @ 90°C Sn (0.75 mm²)
Number of Pins: around 200 for 2 module headers
Pin Classes / Surface: 0.5 mm 1.2 mm / Sn***, Ag, Au
Joining technology PCB: Press-Fit technology (preferred)
Ethernet Functionality: acc. to Open Alliance TC2 / TC9
Connector supplier: BOSCH, Sumitomo, APTIV
*:Specification has to be confirmed by wiring harness connector supplier; **: According to specification of used contact system ; ***: Series
Microflex 0.5 – Innovative compact automotive connector interface
Typical specification classes for Microflex interface, other specifications on request
System responsibility within the wiring harness connector supplier

## Slide 4: Ethernet-integration in standard Microflex interface
Microflex 0.5 – Innovative compact automotive connector interface
  Ethernet connectivity which reduces the amount of interfaces/connector plug-in mounts at the OEM
  Usable for sealed and unsealed connectors combined with compactness and functional integration
  Flexibility and scalability of Ethernet function without change of design in standard 4-row/2-row interfaces
Reduction of plug-ins (red. interface-amount)
Flexible mounting place (interface: sealed / unsealed)
Re-use: Pins, connectors, headers
Reduction of material (metal / coating / plastic)
Miniaturization (reduced box volume, more PCB-space) Standardization (new pin- / interface-standard)
All-In-One Interface
9x Power
42x Signal
5x Ethernet
sealed /unsealed
5.5 cm
Example with 5 Ethernet ports

## Slide 5: Flexible wiring harness concepts - standard vs. modular design
Microflex 0.5 All-In-One Interface |  | 
 | sealed | unsealed
100BASE-T1 |  | 
1000BASE-T1 |  | 
UTP |  | 
STP/SPP |  | 
Signal |  | 
Power |  | 
twisted pair cable
contact carrier
“standard”: 100 Mbps
twisted pair cable
0 – 5 x 100 Mbps  76 – 44 Std. signal pins
0 – 5 x 100(0) Mbps  74 – 42 Std. signal pins
Modular contact carrier design for plug-in modules automatic assembly possible
“modular”:
100 Mbit/s / 1 Gbps
Standard application (100 Mbps/UTP)
Modular design for twisted pair cables w. option for automated assembly (100 Mbps/1 Gbps w. UTP/STP )
Development ongoing for Multi-Gig Ethernet application (up to 10 Gbit/s)
Typical UTP & STP Ethernet cables
(e.g. Kroschu Krocar 6499-6795, Leoni Dacar 647-4)
Microflex 0.5 – Innovative compact automotive connector interface
Ethernet

## Slide 6: Scalability of Ethernet ports – 100 Mbps / 1Gbps (Example)
Microflex 0.5 – Innovative compact automotive connector interface
twisted pair cable
Full scalability of Ethernet ports – modular design for easy application and save function
Example Interface
no Ethernet-port
1 Ethernet-port
5 Ethernet-ports
scalable to
74 -48 x Signalpin
0 – 5 x 100 Mbps
0 – 5 x 1 Gbps
Contact carrier modular design
100 Mbps: unshielded (plastic)
1 Gbps: shielded (metal)
Ethernet
Ethernet